## Slide 1: Software Defined Networking How it has transformed networking and what happens next
Nick McKeown 马格理 Stanford University

## Slide 2: Ethane project:
2006
35,000 users
10,000 new flows/sec
137 network policies
2,000 switches
2,000 switch CPUs
Stanford campus
How difficult is it to write the control software for our network?

## Slide 3: Crazy question: What if software decides whether to accept each flow, and how to route it?
A
B
[Sigcomm ’07, Kyoto]
Controllers
Check flow against policy
Pick route

## Slide 4: How many servers do we need for 35,000 users?

## Slide 5: Answer:
less than one

## Slide 6: If we can define network behavior outside the datapath, then eventually we will.

## Slide 7: Computer Industry
Proprietary
Operating System
Proprietary
Hardware
Proprietary
Applications
App
App
App
App
App
App
App
App
App
App
App
Open Interface
Linux
Mac
OS
Windows
(OS)
or
or
Open Interface
Disaggregation
Microprocessor

## Slide 8: Networking Industry
Proprietary
Operating System
Proprietary
Hardware
Proprietary
Features
App
App
App
App
App
App
App
App
App
App
App
Open Interface
Open Interface
Control Plane 1
Control Plane 2
NOX
Beacon
ONIX
POX
ONOS
Flood light
Trema
ODL
Ryu
Merchant Switch Chips
Disaggregation

## Slide 9: 2008
Problem: Network innovation controlled by router vendors.
Consequence: Glacially slow innovation of the Internet.
Solution
Network owners and operators write the software to control their networks.

## Slide 10: Software Defined Networks
Part 1: Network owners and operators now define the software to control their network.

## Slide 11: SDN was inevitable because…
Rise of Linux.
Rise of whitebox servers and data centers.
Rise of merchant switching silicon.

## Slide 12
Applications
OS
CPU
x86
Applications
Linux
Applications
OS
CPU + ASIC
x86 + ASIC
Control Programs
Linux
Servers
Network switches
Legacy
Whitebox
Legacy
Whitebox

## Slide 13: Example: Big Data Center
Cost
500,000 servers
25,000 switches
$10k per legacy switch = $250M
$2k disaggregated switch = $50M
Savings in 5 data centers = $1Bn
Control
Centralized remote control is easier
“Centralize if you can, distribute if you can’t”
Customized, differentiated network
Home grown traffic engineering
50% utilization → 95% utilization

## Slide 14: All networking equipment is disaggregating
5G Gateways and Basestations
Optical and Metro Transport
WiFi Access Points
Residential broadband access
Enterprise network equipment: switches, routers, firewalls
“Software is eating the world (of networking)”

## Slide 15: Now I can tailor my network to meet my needs!
I can….
Quickly deploy new protocols.
Monitor precisely what my forwarding plane is doing.
Fold expensive middlebox functions into the network, for free.
Try out beautiful new ideas. Tailor my network to meet my needs.
Differentiate. Now I own my intellectual property.

## Slide 16: But wait a minute…
Everything on the last slide is untrue!

## Slide 17
Switch OS
OSPF
BGP
etc.
Driver
New

## Slide 18
Network Equipment Vendor
Network Owner
ASIC
Team
Software
Team
Feature
Weeks
Years
Years
Feature
Feature

## Slide 19: Network systems are built “bottoms-up”
Switch OS
Fixed-function switch
Driver
“This is how I process packets …”
ASIC

## Slide 20: “Programmable switches are 10-100x slower than fixed-function switches. They are more expensive and consume more power.”
Conventional wisdom in networking
Not true any more!

## Slide 21: 2018
Problem: Network innovation controlled by chip vendors.
Consequence: Glacially slow innovation of the Internet.
Solution
Network system developers write the software
to process packets in their networks.

## Slide 22: Software Defined Networks
Part 2: Network system developers take
control of how packets are processed too

## Slide 23: Network systems are starting to be programmed “top-down”
Programmable Switch
Driver
Switch OS
“This is precisely how you must process packets”

## Slide 24: Why are programmable forwarding planes happening now?

## Slide 25: Domain Specific Processors
CPU
Computers
Java
Compiler
GPU
Graphics
OpenCL
Compiler
DSP
Signal
Processing
Matlab
Compiler
Machine
Learning
?
TPU
TensorFlow
Compiler
Networking
?
Language
Compiler
>>>

## Slide 26: Domain Specific Processors
CPU
Computers
Java
Compiler
GPU
Graphics
OpenCL
Compiler
DSP
Signal
Processing
Matlab
Compiler
Machine
Learning
?
TPU
TensorFlow
Compiler
PISA
Networking
P4
Compiler
>>>

## Slide 27
Match+Action Stage
Memory
ALU
Programmable Parser
Programmable Match-Action Pipeline
PISA: Protocol Independent Switch Architecture

## Slide 28
PISA: Protocol Independent Switch Architecture

## Slide 29: Example P4 Program
Memory
ALU
Programmable Parser
Programmable Match-Action Pipeline
header_type ethernet_t { … }
header_type l2_metadata_t { … }
header ethernet_t ethernet;
header vlan_tag_t vlan_tag[2];
metadata l2_metadata_t l2_meta;
Header and Data Declarations
Parser Program
parser parse_ethernet { extract(ethernet); return switch(ethernet.ethertype) { 0x8100 : parse_vlan_tag; 0x0800 : parse_ipv4; 0x8847 : parse_mpls; default: ingress; }
Tables and Control Flow
table port_table { … }
control ingress { apply(port_table); if (l2_meta.vlan_tags == 0) { process_assign_vlan();
} }

## Slide 30: P4 PISA chips starting to emerge (2016)
Programmed using P4
Same power, performance & cost as fixed-function switches
Programs always run at line-rate
Several P4-programmable devices will emerge in next 2-3 years.
My prediction: Within 5 years, all switches will be programmable.
Notes: Actual END POINT of talk

## Slide 31: How programmability is being used
Reducing complexity
1

## Slide 32: Reducing complexity
Compiler
Programmable Switch
Driver
Switch OS
switch.p4
IPv4 and IPv6 routing
- Unicast Routing
- Routed Ports & SVI
- VRF
- Unicast RPF - Strict and Loose
- Multicast
- PIM-SM/DM & PIM-Bidir
Ethernet switching
- VLAN Flooding
- MAC Learning & Aging
- STP state
- VLAN Translation
Load balancing
- LAG
- ECMP & WCMP
- Resilient Hashing
- Flowlet Switching
Fast Failover
– LAG & ECMP
Tunneling
- IPv4 and IPv6 Routing & Switching
- IP-in-IP (6in4, 4in4)
- VXLAN, NVGRE, GENEVE & GRE
- Segment Routing, ILA
MPLS
- LER and LSR
- IPv4/v6 routing (L3VPN)
- L2 switching (EoMPLS, VPLS)
- MPLS over UDP/GRE
ACL
- MAC ACL, IPv4/v6 ACL, RACL
- QoS ACL, System ACL, PBR
- Port Range lookups in ACLs
QOS
- QoS Classification & marking
- Drop profiles/WRED
- RoCE v2 & FCoE
- CoPP (Control plane policing)
NAT and L4 Load Balancing
Security Features
- Storm Control, IP Source Guard
Monitoring & Telemetry
Ingress Mirroring and Egress Mirroring
Negative Mirroring
Sflow
INT
Counters
Route Table Entry Counters
VLAN/Bridge Domain Counters
Port/Interface Counters
Protocol Offload
- BFD, OAM
Multi-chip Fabric Support
- Forwarding, QOS

## Slide 33: Reducing complexity
Compiler
Driver
Switch OS
My switch.p4
Programmable Switch

## Slide 34: How programmability is being used
Adding new features
2

## Slide 35: Adding features: Some examples so far
New encapsulations and tunnels
New ways to tag packets for special treatment
New approaches to routing: e.g. source routing in MSDCs
New approaches to congestion control
New ways to process packets: e.g. processing ticker-symbols

## Slide 36: Example new applications using P4
Example #1: Layer-4 Load Balancer

## Slide 37: Today: Hardware Layer 4 Load-balancing
Hardware Load Balancers
Application Servers
Clients
>$200+k each

## Slide 38: Today: Software Layer 4 Load-balancing
Software Load Balancers
Application Servers
Clients

## Slide 39: P4 Example: Layer 4 Load-balancing
Software Load Balancers
Application Servers
Clients
P4 Program

## Slide 40: Example new applications using P4
Example 1: Layer-4 Load Balancer
  Replace 200 servers with one switch chip
  Operates at 6.5Tb/s
  All packets load-balanced in < 1ms
  Up to 10 million http flows
Publication SilkRoad: Making Stateful Layer-4 Load Balancing Fast and Cheap Using Switching ASICs. Rui Miao et al. ACM Sigcomm 2017

## Slide 41: Example new applications using P4
Example #2: Fast Firewall and Audit Trail
  Add over 1M new firewall entries per second
  Create audit record for every new flow and firewall entry
  Firewall now inline, at 6.5Tb/s and <1ms

## Slide 42: Other P4 Applications
World’s fastest key-value store cache
World’s fastest DNS cache (to prevent DDoS)
World’s fastest storage network cache
World’s fastest consensus protocol for distributed applications
<Your beautiful new idea here!>

## Slide 43: How programmability is being used
Network telemetry
3

## Slide 44
“Which path did my packet take?”
1
“Which rules did my packet follow?”
2
“In Switch 1, I followed rules 75 and 250. In Switch 9, I followed rules 3 and 80. ”
# | Rule
1 | 
2 | 
3 | 
… | 
75 | 192.168.0/24
… | 
“I visited Switch 1 @780ns, Switch 9 @1.3µs, Switch 12 @2.4µs”

## Slide 45
“How long did my packet queue at each switch?”
3
“Delay: 100ns, 200ns, 19740ns”
Time
Queue
“Who did my packet share the queue with?”
4

## Slide 46
“How long did my packet queue at each switch?”
3
“Delay: 100ns, 200ns, 19740ns”
Time
Queue
“Who did my packet share the queue with?”
4
Aggressor flow!

## Slide 47: We’d like the network to answer these questions
“Which path did my packet take?”
“Which rules did my packet follow?”
“How long did it queue at each switch?”
“Who did it share the queues with?”
1
2
3
4
With P4+PISA we can answer all four questions for the first time. At full line rate. Without generating additional packets.

## Slide 48: Viewing Microbursts (to the nanosecond)

## Slide 49: How programmability is being used
3
2
Reducing complexity
Adding new features
Network telemetry
1

## Slide 50: In summary…
SDN is about who is in control! Part 1: Network owners decided how their networks are controlled. Part 2: Next, they will decide how packets are processed.
Chip technology: From now on, programmable forwarding will have the same power, performance and cost as fixed function.
New ideas: Beautiful new ideas are now owned by the programmer, not the chip designer.

## Slide 51: Thank you!
Visit www.p4.org for more information